A Work Energy Servo Apparatus

for the Physics 128/241 Laboratory Courses

- Tomasch

February 2006

Procurement

2/10/06 The following items are being procured, with McMaster Carr as the first-choice vendor.  Thirty five units are to be manufactured.

- Two Meter long aluminum scales (McMaster Part #1971A58)

- Angle brackets, U-Brackets for table mounting.  Current setup uses 4” corner brackets, but McMaster Carr may offer better alternatives.

- C-channel stock, 6’ long.  Current part is a shelf mounting rail, but aluminum C-channel stock with a 1/16” web thickness should be explored.  A wider C-channel will permit mounting the channel along the scale center line.

- C-Clamps for attachment to the laboratory benches.  The current examples are satisfactory.  A deep-throat type is needed for the bottom attachment point.

- Male banana plugs, red and black

- Silicone clad wire, typical of DVM probe leads for the electrical interface.  The pigtails exiting the modified servos will need to be a smaller diameter; the splice will be made with heat shrink tubing.  Leads will be strain relieved to the experiment spine with cable ties and tie pads.

- ½” square black cable tie pads

- 10 additional servos (ADT)

- 10 additional spools (ADT)

- Fasteners—¼-20 Button socket cap screws for mounting

C-channel and brackets to the aluminum scale (ADT)

- J bolts and cylindrical metal canisters (to be filled with lead shot) for standard masses.  Possible items might metal “match safes”, aluminum cigar tubes or ???

Servo Modification:  The servos can now be modified to the point of having the amplifiers removed, the limit stops trimmed and standard pigtail leads soldered to the motor and exiting the case.  The critical path item is solder wick, which is needed to properly unsolder the motors from the amplifier boards.  This is to be procured ASAP.  The next step after this is to modify the output wheels, which require slight trimming with an X-Acto knife and drilling to accept the fasteners which retain the spool.  The spools can then be mounted.  ADT will supervise all fabrication/modification activities.

Bill of Materials

To Construct One Unit:

One Required:

| 1971A58 | Aluminum Rule Metric Grads, 200 CM Length, 2" Width, 1/8" Thick | $16.25 |
| --- | --- | --- |

One Required:

| 47065T122 | Fractional T-Slotted Framing System 1" X 1" Square Extrusion, 6' Length | $20.70 |
| --- | --- | --- |

Three Required:

| 1556A17 | Steel Corner Brace Zinc-Plated, 4" Length Of Sides, 7/8" Width | $1.26 |
| --- | --- | --- |

Eight Required (Must be purchased in packages of 15)

| 47065T142 | Fractional T-Slotted Framing System Steel T-Nut W/Cap Screw for 1" SQ & 1" X 2" Extrusion, Packs of 15 | $9.16 |
| --- | --- | --- |

Two Required (Must be purchased in packages of 100)

| 91255A540 | Alloy Steel Button Head Socket Cap Screw 1/4"-20 Thread, 3/4" Length, Packs of 100 | $13.91 |
| --- | --- | --- |

Eight Required (Must be purchased in packages of 100)

| 91255A539 | Alloy Steel Button Head Socket Cap Screw 1/4"-20 Thread, 5/8" Length, Packs of 100 | $13.32 |
| --- | --- | --- |

Eight Required (Must be purchased in packages of 25:

| 98029A029 | Black-Oxide Steel Thick Flat Washer 1/4" Screw Sz, 9/32" Id, 5/8" Od, .110" - .135" Thk, Packs of 25 |
| --- | --- |

Two Required (Must be purchased in packages of 50):

| 95479A111 | Grade 5 Black Oxide Steel Hex Nut 1/4"-20 Screw Size, 7/16" Width, 7/32" Height, Packs of 50 | $8.13 |
| --- | --- | --- |

One Required:

| 5038A2 | Light-Force Iron C-Clamp Deep Pattern, 1-1/2" Max-0" Min Open, 300# Hold Cap | $7.01 |
| --- | --- | --- |

One Required:

5133A13

Light-Force Iron C-Clamp Reg Pattern, 2" Max-0" Min Open, 400# Holding Cap In stock at $2.06 Each

One Required:

| Futaba S3003 Servo Standard | Manufacturer Stock# S3003 Special Stock# LXH288 Tower's Low Price 10.99 Stock Status In Stock |
| --- | --- |

One Required:  Custom Spool

Neoprene Rubber Sheet for Contact Surfaces of Mounting Brackets:

| 8525T31 | 1/16" Thick, 12" X 12", Neoprene Rubber Sheet Gasket | $3.52 |
| --- | --- | --- |