An Inexpensive Clothespin Microwave Transmitter and Receiver

Steven Wilser, Department of Physics, SUNY- Buffalo State College

<wilssm14@mail.buffalostate.edu> 716.200.7466

This project studied and mapped the electric field produced by a microwave spark gap antenna constructed from low cost apparatus and supplies. A spark gap microwave transmitting antenna made from a household clothespin was driven by a high voltage current limited power supply. A receiving antenna made from copper wire was used to detect the electric field, where the intensity of the field was displayed on a multimeter. A low cost reflector was used to create standing waves within the electric field which enabled measurement of the wavelength of the radiation by measuring the distance between nodes.  Linear arrays of wire were used as polarizers to analyze the E field.

References:

Pine, J., & King, J., & Morrison, P., & Morrison, P., (1996). Zap!: Experiments in electrical currents and fields. Boston, MA: Jones and Bartlett.

Experiment 3: Hertz’s microwave experiment. Retrieved June 6, 2007, from web.mit.edu/8.022/www/labs/lab3.pdf.

A microwave generator, receiver, and reflector. Retrieved June 6, 2007, from ocw.mit.edu/NR/rdonlyres/Physics/8-022Fall-2004/D9D35AB5-86FA-4651-9B51-EA8660685CEE/0/lab3.pdf.

Funded by the Early Undergraduate Research Program at SUNY- Buffalo State College PI: J Singer.  Advisor: D. MacIsaac.