Stadium Horn

Materials

* 2 9 inch long 5/8 inch OD

1⁄2 ID CPVC pipe

* 1⁄2 inch connector

* 3/8 inch drill bit

* 1⁄2 inch drill bit

* 5/8 inch drill bit

* Drill

* 35 mm film canister

* small square of plastic grocery bag

Construction

* Cut 2 9 inch pieces of 5/8 inch OD CPVC

* Next you are going to drill three holes in the 35 mm film canister and lid

* The hole in the canister side and the hole in the lid are 5/8 inch.  The hole in the bottom end of the canister is 1⁄2 inch.

* Take a small square of plastic grocery bag and put it between the lid and the canister and snap on the lid.  The plastic should be taught.

* Drill a 3/8 inch hole in the center of the length of each 9 inch piece of pipe.

* Slide the 1⁄2 inch hole in the bottom of the canister on to one of the sections of 9 inch long CPVC pipe.

* Use the connector to connect the two pieces of pipe.

* Make the pipe touch lightly against the grocery back-Not too tight not too loose.

* Put your mouth over the hole in the side of the canister and blow.

* Pitch can be adjusted by covering up the 3/8 inch holes with your fingers while you blow and by disconnecting the two pipes.

23Sep2006 SUNY-Buffalo State College
Western New York Physics Teachers’ Alliance <http://physicsed.buffalostate.edu/WNYPTA/>